## Slide 1: CS 31007 Autumn 2021 COMPUTER ORGANIZATION AND ARCHITECTURE
Indian Institute of Technology Kharagpur
Computer Science and Engineering
Instructors
Rajat Subhra Chakraborty (RSC)
Bhargab B. Bhattacharya (BBB)
Lecture # 7
CPU Performance Equation, Amdahl’s Law, Die Yield
19 August 2021
Notes: Good Morning!
The title of today’s talk is “On some Planar Partitioning Problems”.

## Slide 2: What determines the execution time of a machine/assembly-level program P when it is run on a machine M?
P consists of a number of machine-level instructions (IC: instruction count);
Each machine instruction requires several clock cycles to complete (CPI: average number of clock cycles per instruction);
Each clock cycle has certain time period (CCT: clock cycle time)
Thus, CPU-time = IC  CPI  CCT
(CPU Performance Equation);
Performance  1/CPU-time

## Slide 3: CPU Clocking
CPUs are driven by constant-rate system clocks:
  100 MHz clock frequency (f) means the system clock ticks 100 million times every second:
One Clock Cycle Time (“Tick”), i.e., CCT
= 1/100,000,000 sec
=1/100 microsec = 10 nanosec
CCT = 1/f
Clock (cycles)
Data transfer and computation
Update state
Clock period
CCT

## Slide 4: What determines the clock frequency for a processor?
original image
Time period of pulsating heart (contraction and relaxation) should be just large enough so that blood reaches to the farthest extremities in one pumping cycle
460
245
200
72
30
# heart-beats per minute  clock period
= clock cycle time (CCT)
clock frequency (f) = 1/CCT

## Slide 5: Clock Timing
original image
Clock period should be large enough to accommodate delays along critical paths in the circuit (longest ones);
but should not be too large – system slows down unnecessarily
critical path
CCT > signal delay along the longest sensitizable logic path (critical path) among those from PI/outputs(FFs)  PO/inputs(FFs)

## Slide 6
clock

## Slide 7: Power Issues and CCT
In CMOS IC technology
§1.7 The Power Wall
×1000
~×40
5V → 1V

## Slide 8
Mem

## Slide 9: CPU Time
Performance improved by
  Reducing number of clock cycles
  Increasing clock rate (a.k.a. frequency)
  Hardware designer must often trade off clock rate against cycle count

## Slide 10: CPU Time Example
Computer A: 2GHz clock, 10s CPU time
Designing Computer B
  Aim for 6s CPU time
  Can do faster clock, but causes 1.2 × clock cycles
How fast must Computer B clock be?

## Slide 11: Instruction Count and CPI
Instruction Count for a program
  Determined by program, ISA and compiler
Average cycles per instruction
  Determined by CPU hardware
  If different instructions have different CPI
    Average CPI affected by instruction mix

## Slide 12: CPI Example
Computer A: Cycle Time = 250ps, CPI = 2.0
Computer B: Cycle Time = 500ps, CPI = 1.2
Same ISA
Which is faster, and by how much?
A is faster…
…by this much

## Slide 13: CPI in More Detail
If different instruction classes take different numbers of cycles
Weighted average CPI
Relative frequency

## Slide 14: CPI Example: Who is better?
Two compiled codes for the same problem, using instructions in classes A, B, C
Class | A | B | C
CPI for class | 1 | 2 | 3
IC for Programmer 1 | 2 | 1 | 2
IC for Programmer 2 | 4 | 1 | 1
Sequence 1: IC = 5
  Clock Cycles = 2×1 + 1×2 + 2×3 = 10
  Avg. CPI = 10/5 = 2.0
Sequence 2: IC = 6
  Clock Cycles = 4×1 + 1×2 + 1×3 = 9
  Avg. CPI = 9/6 = 1.5

## Slide 18: Performance Summary
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, CCT
  CPI is also affected by memory hierarchy, pipelining; CCT is affected by logic design, technology
The BIG Picture: CPU Performance Equation
CPU-time = IC  CPI  CCT

## Slide 19: Reducing Power
Suppose a new CPU has
  85% of capacitive load of old CPU
  15% voltage and 15% frequency reduction
The power wall
  We can’t reduce voltage further
  We can’t remove more heat
How else can we improve performance?

## Slide 20
How to improve the performance of a machine by “Enhancement” of one or more components?
 Amdahl’s Law
How to improve the performance of a computing system by adding more processors (cores)?
 Gustavson-Barsis Law

## Slide 21: Example: Improving performance in steps
Old machine Mold
New machine Mnew (improved a.k.a. (enhanced)
Speed-up for component C
= 2
Cold
Cnew
responsible for 1/3 of CPU-time
Question: What is the overall speed-up of Mnew w.r.t. Mold?

## Slide 22
Gradual enhancement of resources for speed-up
Let C be a component (e.g., adder) of an old machine, which is improved to C’ in a new machine
A job submitted to the old machine takes 60 secs to finish

## Slide 23
Gradual enhancement of resources for speed-up
2

## Slide 24
The general result concerning the overall speed-up, when a component of the old machine is enhanced is captured in “Amdahl’s Law”
Gene Amdahl
(1922-2015)

## Slide 25: Amdahl's Law
Speed-up due to enhancement E:
CPU-time w/o E Performance w/E
Speed-up(E) = ------------- = ------------------
CPU-time w/E Performance w/o E
Suppose that enhancement E accelerates a fraction F of the task by a factor S, and the remainder of the task is unaffected
F

## Slide 26: Amdahl’s Law
CPU-timenew = CPU-timeold × (1 - Fracenhanced) + Fracenhanced
Speed-upoverall =
CPU-timeold
CPU-timenew
Speed-upenhanced
=
1
(1 - Fracenhanced) + Fracenhanced
Speed-upenhanced
Law of diminishing return: unaffected fraction will determine the limiting case!
Improvement of larger fraction will yield higher overall speed-up  Make the common case faster

## Slide 27: Example: Amdahl’s Law
Floating-point (FP) instructions are improved to run 2X in a new machine
10% of actual instructions are FP

## Slide 28: Example: Amdahl’s Law
Speed-upoverall
=
1
0.95
=
1.053
CPU-timenew = CPU-timeold × (0.9 + 0.1/2) = 0.95 × CPU-timeold
Floating-point (FP) instructions are improved to run 2 in a new machine
10% of actual instructions are FP
For FP Speed-up 100X, Speed-upoverall
=
1.109

## Slide 29: Pitfall: Amdahl’s Law
Improving an aspect of a computer and expecting a proportional improvement in overall performance
§1.10 Fallacies and Pitfalls
  Can’t be done!
Example: multiply accounts for 80s/100s
  How much improvement in multiply performance to get 5× overall?
Corollary: Make the common case fast

## Slide 30: Multiprocessors
Multicore microprocessors
  More than one processor per chip
  Clock frequency limited
Requires explicitly parallel programming
  Compare with instruction level parallelism
    Hardware executes multiple instructions at once
    Hidden from the programmer
  Hard to do
    Programming for performance
    Load balancing
    Optimizing communication and synchronization

## Slide 31: Parallelism: Adding multiple processors
What kind of speed-up is expected?
s: time needed by a single processor on serial parts of P;
p: time needed by a single processor on the parts of P that can be parallelized; s + p = 1
By Amdahl’s Law, the speed-up in the multi-core processor
= 1/(s +p/N) If s = 10%, the maximum speed-up is 10X
Single processor
Multi-processor
1. X:= A + B
2. Y:= X * C
3. D:= B + C
4. E:= X – C
Statement 1 & 2 cannot be executed in parallel (serial);
1 and 3 can be executed in parallel; 2 & 4 can be done in parallel
Pessimistic view

## Slide 32: Parallelism: Adding multiple processors Amdahl’s Law versus Gustavson-Barsis Law
By Amdahl’s Law, the speed-up in the multi-core processor
= 1/(s +p/N), i.e., it is limited by s, increasing N does not help.
Let s and p represent serial and parallel time on N-core system; The single core processor would take s + (p × N) time to perform the same job P.
Hence, Speed-up = (s + (p × N))/(s + p) = (s + (p × N)
Thus, by Gustavson-Barsis Law, speed-up grows with N
In Amdahl’s Law, the size of the job is assumed to be constant;
however, multi-cores can solve a large job in the same time.
This leads to Gustavson-Barsis Law:
Optimistic view

## Slide 33: Metrics of Performance
Compiler
Programming
Language
Application
Datapath
Control
Transistors
Wires
Pins
ISA
Function Units
(Millions) of Instructions per second: MIPS
(Millions) of (FP) operations per second: MFLOP/s
Cycles per second (clock rate)
Megabytes per second
Throughput per month
Operations per second

## Slide 34: ISA: RISC versus CISC
RISC (Reduced Instruction Set Computing)
  Keep the instruction set small and simple
  Fixed instruction lengths, easy encoding
  Load-store instruction sets; register-indirect addressing with offset; ALU operations involve only registers
  lw $t1 - 40($t2); add $t0,$s1,$s2
  Limited addressing modes
  Limited operations
  IC high, CPI low
  Advantage: enables hardware simple and fast; decoding simple; pipelining easy, die-area small
  Performance is optimized focused on software

## Slide 35
RISC Example: MIPS, Sun SPARC, HP PA-RISC, IBM PowerPC, Alpha, RISC-V, ARM
CISC - Complex Instruction Set Computer
- complex instructions, encoding non-uniform
- different lengths
- can handle multiple operands
- complex functionalities
- IC low, CPI high
pipelining becomes harder; hardware cost increases; compiler design becomes more involved;
Examples of CISC processors are Intel CPUs, System/360, VAX, AMD
Notes: As opposed to CISC – Complicated Instruction Set Architecture (ala the x86)

## Slide 36: Eight Great Ideas
Design for Moore’s Law
Use abstraction to simplify design
Make the common case fast
Performance via parallelism
Performance via pipelining
Performance via branch prediction
Hierarchy of memories
Dependability via redundancy
§1.2 Eight Great Ideas in Computer Architecture
Amdahl’s law
Gustavson-Barsis law

## Slide 37: Intel Core i7 Wafer
300mm wafer, 280 dies, 32nm technology, 4-8 cores per die
Each die is 20.7 x 10.5 mm
Intel Xeon E5-2600 v4 chips with 22 processors, 14nm process technology (2016)
wafer
chip
die
Estimation of Die Yield

## Slide 38: Defects in IC’s and Yield
defects on chips make them unusable;
peripheral chips are incompletely fabricated, and hence unusable (square-peg in round-hole problem);
yield: fraction of good chips produced;
chip-cost depends on yield;

## Slide 39: Integrated Circuit Cost
Nonlinear relation to area and defect rate
  Wafer cost and area are fixed
  Defect rate determined by manufacturing process
  Die area determined by architecture and circuit design
[1 + {(Defects per unit area of chip × chip area)/}]
This is an empirical estimation of yield;  is a parameter that roughly captures the complexity of the manufacturing process
chip-cost ~ (die-area)4

## Slide 45: Concluding Remarks
Cost/performance is improving
  Due to underlying technology development
Hierarchical layers of abstraction
  In both hardware and software
Instruction set architecture
  The hardware/software interface
Execution time: the best performance measure
Power is a limiting factor
  Use enhancement and parallelism to improve performance
§1.9 Concluding Remarks

## Slide 46: Next Class
Introducing MIPS Assembly Language
Notes: Good Morning!
The title of today’s talk is “On some Planar Partitioning Problems”.

## Slide 47: CS 31007 Autumn 2021 COMPUTER ORGANIZATION AND ARCHITECTURE
Indian Institute of Technology Kharagpur
Computer Science and Engineering
Announcement for Test-01
Monday, 06 September 2021, 12 noon – 2 pm
Exam will be conducted via CSE Moodle
Coverage: Processor Design Basics, von Neumann Architecture,
ISA, RISC/CISC, CPU-Performance, Die Yield,
MIPS Assembly Language Programming
(Material covered till 02 September 2021)
Notes: Good Morning!
The title of today’s talk is “On some Planar Partitioning Problems”.